## Slide 1
Memory Polynomial-Inspired Neural Network for
Modeling the Power Amplifier Non-linearities
Team MLAP
- Pedamalli Saikrishna
- Ashok Kumar Reddy Chavva
- Boddapati Hari Krishna
Beyond 5G Team
Samsung R&D Institute Bangalore
ML5G-PS-007:Non-linear Power Amplifier Behavioral Modeling to achieve higher energy efficiency in 5G RAN

## Slide 2
Introduction – Power Amplifier in Wireless Communication
Power Amplifier Requirement
  Power Amplifier boosts the base band signal before transmitting.
  Helps the signal reach receiver overcoming the path loss.
Challenges
  Exhibits non-linear behaviour when operated at higher power.
  This non-linearity affects signal quality and also causes inter channel interference.
PA
Modulator
Transmitter
Demodulator
Signal to be transmitted
Received Signal
Receiver
Wireless Channel
Tx Antenna
Rx Antenna
Ideally, we want to be
where, corresponds to the PA Gain
PA

## Slide 3
Introduction – Power Amplifier Non-linearities
Power Amplifier Non-linearity
  AM – AM Characteristics.
    Output amplitude varies non-linearly with input amplitude.
  AM – PM Characteristics.
    Phase shift in signal.
  Memory.
    Past samples having an effect on current sample output.

## Slide 4
Problem Statement – Modeling Power Amplifier Non-linearities
Power Amplifier Modeling
  Model should predict the output sequence of the PA given input sequence of data.
  The output includes non-linear effect, short term and long term memory effect.
  The output , depends on {non-linear and memory effect}
  Let = .
  Then, the problem boils down to finding the appropriate that maps to
Significance of Power Amplifier Modeling
  Helps in understanding the distortions caused to the signal due to non-linearity introduced by the PA
  Helps in designing algorithms to compensate for the distortions caused by the non-linearity.
  Improves the quality of received signal.
  Improves the efficiency of the wireless communication systems.

## Slide 5
Literature Survey
Power Amplifier Models
  Memoryless non-linear models
  Non-linear models with linear memory
  Non-linear models with non-linear memory
Memoryless non-linear models
Non-linear models with non-linear memory

## Slide 6
Proposed Solution – Network Architecture
Salient Features
  Priority based on chronology of samples.
  Low complex – exploiting conventional math model
  Adaptive non-linear power terms for each sample
Network Hyper parameters
  K = 2
  M = 11
  HL1 C = 9.
  HL1 P = 5.
  HL2 C = 5.
  HL2 P = 2.
  HL3 = 10.
  HL 4 = 20.
  HL 5 = 10.
  OL = 2.

## Slide 7
Proposed Solution – Training the Network
Hyper-parameters | Value
Optimizer | Adam
Batch size | 200
Epochs | 3000
Loss function | MSE
Loss Function
Training Phase
  Obtain () pairs of the PA.
  Normalize both () with the max of
  Use the normalized pairs for training the network.
  Save the model parameters
Testing Phase
  Obtain the PA input () of the test dataset.
  Normalize ( using the same normalizing factor as training max().
  Use this as the network input and predict the output using the trained network.
  The output is then multiplied with to obtain the predicted PA output (.

## Slide 8
Results – Dataset and Metrics
Datasets
  Training set – 183964.
  Testing set – 40000.
    1 – 20000 samples and 20000 – 40000 samples diff avg power
  Testing set 2 – 40000.
    1 – 20000 samples and 20000 – 40000 samples diff avg power
  Testing set 3 – 65536.
  Testing set 4 – 65536.
NMSE
ACEPR
  Step 1
  Step 2
  Step 3
  Step 4

## Slide 9
Results – Performance Metrics (NMSE and ACEPR) and Complexity Analysis
Dataset | NMSE (dB) | ACEPR (dB)
Train | -32.1 | -44.23
Test 1 – Complete | -33.56 | -44.27
Test 1 – Part 1 | -34.52 | -46.12
Test 1 – Part 2 | -28.97 | -43.52
Test 2 – Complete | -30 | -43.26
Test 2 – Part 1 | -28.43 | -42.71
Test 2 – Part 2 | -30.3 | -46.64
Test 3 | -33.71 | -46.3
Test 4 | -33.33 | -43.56
20 % better compared to next best
Layer | I/P Nodes | O/P Nodes | No. Layers | Real Mul
HL1 C | 4 | 9 | 1 | 36
HL1 P | 4 | 5 | 11 | 220
HL2 C | 9 | 5 | 1 | 45
HL2 P | 5 | 2 | 11 | 110
HL3 | 27 | 10 | 1 | 270
HL4 | 10 | 20 | 1 | 200
HL5 | 20 | 10 | 1 | 200
OL | 10 | 2 | 1 | 20
Total Real Multiplications |  |  |  | 1101

## Slide 10
Results – Performance Metrics (NMSE and ACEPR)
Dataset | Old – LReLU for FCL |  | New – tanh for FCL |  | Improvement | 
 | NMSE (dB) | ACEPR (dB) | NMSE (dB) | ACEPR (dB) | NMSE (dB) | ACEPR (dB)
Train | -32.1 | -44.23 | -32.84 | -45.6 | 0.74 | 1.37
Test 1 – Complete | -33.56 | -44.27 | -34.97 | -45.68 | 1.41 | 1.41
Test 1 – Part 1 | -34.52 | -46.12 | -36.41 | -48.57 | 1.89 | 2.45
Test 1 – Part 2 | -28.97 | -43.52 | -29.35 | -45.77 | 0.38 | 2.25
Test 2 – Complete | -30 | -43.26 | -30.29 | -44.45 | 0.29 | 1.19
Test 2 – Part 1 | -28.43 | -42.71 | -28.39 | -44.36 | -0.04 | 1.65
Test 2 – Part 2 | -30.3 | -46.64 | -30.64 | -48.51 | 0.34 | 1.87
Test 3 | -33.71 | -46.3 | -34.68 | -48.46 | 0.97 | 2.16
Test 4 | -33.33 | -43.56 | -33.77 | -45.37 | 0.44 | 1.81
Avg | -31.66 | -44.51 | -32.37 | -46.31 | 0.71 | 1.8
A further improvement of 0.71 dB and 1.8 dB in NMSE and ACEPR, respectively.

## Slide 11
Conclusion
Proposed a neural network for PA modeling with chronology based priority for samples.
Improved performance with lower complexity.
Activation function when changed from LReLU to tanh in fully connected part (modeling memory part) resulted in improved performance.
Conclusion and Future Work
Future Work
Using the PA model to compensate for non-linearity using DPDs.
Thereby, improving the signal quality and efficiency of the wireless communication system.

## Slide 12
[1] Lei Ding, G. T. Zhou, D. R. Morgan, Z. Ma, J. S. Kenney, J. Kim, and C. R. Giardina, “A robust digital baseband predistorter constructed using memory polynomials,” IEEE Transactions on Communications, vol. 52, no. 1, pp. 159-165, Jan. 2004, doi: 10.1109/TCOMM.2003.822188.
[2] P. Saikrishna, A. Goyal, A. Kumar, A. K. R. Chavva, S. Kim and S. Lee, “Memory Polynomial-Inspired Neural Network to Compensate the Power Amplifier Non-linearities,” Accepted in IEEE Personal, Indoor and Mobile Radio Communications Conference, 2022.
References